## Slide 1: Smart Room Controller – TLM Based ESLD Project
SystemC + TLM‑2.0 based smart environment controller
Neethu Jaisan – M.Tech VLSI Design
Amrita Vishwa Vidyapeetham

## Slide 2: Project Overview
Models a Smart Room Controller using SystemC and TLM‑2.0
Reads Temperature, Humidity, and Motion sensor data
Controls fan speed based on environmental conditions
Demonstrates ESL design abstraction

## Slide 3: System Inputs
Temperature Sensor (°C)
Humidity Sensor (%)
PIR Motion Sensor (0/1)
All inputs are sent as TLM transactions from CPU/Testbench

## Slide 4: Decision Logic
1. No motion → Fan OFF
2. Temperature > 30°C → High Speed
3. Humidity > 70% → Medium Speed
4. Otherwise → Low Speed

## Slide 5: Architecture
Testbench (Initiator Socket)
↓
TLM Transaction
↓
Smart Controller (Target Socket)
↓
Decision Logic
↓
Fan Speed Output

## Slide 6: Concepts Demonstrated
Transaction Level Modeling (TLM‑2.0)
Blocking transport (b_transport)
Initiator and Target sockets
System-level decision modeling
Random stimulus verification

## Slide 7: Simulation Flow
Random sensor values generated
Transactions sent via TLM
Controller evaluates thresholds
Fan state updated
Output printed in console

## Slide 8: Conclusion
Demonstrates early-stage ESL modeling
Useful for validating control algorithms before RTL design
Shows how SystemC TLM can model embedded systems efficiently